## Slide 1
PharmaSafe OCR
Automated prescription information extraction
ROI Detection → Handwritten OCR → Drug Name Correction
Technical Documentation Presentation
PharmaSafe OCR
01

## Slide 2
The clinical problem
Handwritten prescriptions are high-variance documents in a safety-critical workflow
Prescriptions are often written quickly, contain abbreviations, use mixed languages, and vary heavily by physician layout. PharmaSafe turns that messy document into structured medication information that can be reviewed and used downstream.
3
target fields: name, dose, type
1,213
detections in pipeline test run
90.8%
TrOCR exact match on test set
Goal: readable, standardized medication data
PharmaSafe OCR
02

## Slide 3
System architecture
A modular three-stage pipeline built for traceability and independent improvement
Conceptual pipeline: prescription image to structured data
1
ROI Detection
YOLO11n
2
Handwritten OCR
TrOCR
3
Drug Correction
DrugBank + Local BD
INTERMEDIATE OUTPUTS
Bounding boxes + class labels
Raw OCR strings per crop
Corrected drug names + confidence
Why modular? each stage can be trained, evaluated, debugged and improved independently.
PharmaSafe OCR
03

## Slide 4
Stage 1 — ROI detection with YOLO11n
Locating medicine name, dose and type regions inside full prescription images
YOLO11n test predictions; colors represent field classes
MODEL CHOICE
YOLO11n was selected because it gives fast single-pass detection, has fewer parameters for the small-data setting, and supports efficient transfer learning.
TRAINING DATA
• 3 Roboflow prescription datasets merged • Labels remapped into medicine_name, medicine_dose, medicine_type • Stratified 70/15/15 split; ~1,200 images total
0.7094
overall mAP@50
0.7840
mean F1 score
0.7959
mean recall
PharmaSafe OCR
04

## Slide 5
Stage 1 performance profile
Detection quality is strongest at the practical IoU@50 threshold
Training curves across 300 epochs
Printed test-set metrics
Chart: 
| Name | Dose | Type | Mean
mAP@50 | 0.6855 | 0.7446 | 0.698 | 0.7094
F1 | 0.7632 | 0.7986 | 0.7887 | 0.784
Losses converge cleanly. The mAP@50-95 values are lower mainly because tight localization is hard with loosely annotated handwritten regions.
PharmaSafe OCR
05

## Slide 6
Stage 2 — handwritten OCR with TrOCR
Reading each cropped text region using a transformer OCR model
TrOCR test samples: green = exact match, red = incorrect
INPUT / OUTPUT
Input: 384×384 RGB crop from Stage 1
Output: raw text string per crop
WHY TROCR?
• Traditional OCR struggles with handwriting • TrOCR is pre-trained for handwritten text • Encoder-decoder design handles variable-length drug names
FINE-TUNING STRATEGY
Stage A: decoder only, 5 epochs
Stage B: full model, lower LR
PharmaSafe OCR
06

## Slide 7
Stage 2 results
Strong word-level performance on handwritten drug names
Validation CER and WER during fine-tuning
90.8%
exact match on test set (830/914)
0.0647
character error rate
0.161
word error rate
~0.91
Drug F1 using rapidfuzz ≥ 90
Main failure mode: visually similar drug names, e.g., cephalosporin antibiotics that look close in handwriting.
Known limitation: numeric dosage OCR can suffer from TrOCR letter bias, e.g., 500mg → SOO mg.
PharmaSafe OCR
07

## Slide 8
Stage 3 — drug name spell correction
Converting raw OCR into standardized pharmaceutical names
Raw OCR text
DrugBank + local BD vocabulary
270,000+ entries
Corrected drug name
+ confidence tier
TWO-PASS ALGORITHM
• Pass 1: exact case-insensitive lookup • Pass 2: fuzzy matching with token_sort_ratio • High confidence ≥95; low confidence 75–94; below 75 stays unrecognized
VOCABULARY COMPOSITION
Generic names
Chemical synonyms
Commercial brands
Local Bangladeshi drug labels
PharmaSafe OCR
08

## Slide 9
Stage 3 impact
Correction improves standardization while flagging uncertain cases
Threshold tuning for precision/recall/F1
Correction status distribution and before/after exact match
73.2%
DrugBank exact match after correction
669 / 914
exact corrected predictions
Low-confidence corrections are intentionally flagged for review instead of silently accepted, which is safer for medical workflows.
PharmaSafe OCR
09

## Slide 10
Full pipeline integration
How one prescription image moves through the system
Full prescription image
YOLO boxes
conf ≥ 0.25
Crop + 4px padding
resize 384×384
TrOCR beam search
4 beams
Drug correction
name fields only
Example full-pipeline prediction on one prescription
FINAL CSV METADATA
dataset, image path, predicted class, bounding box, YOLO confidence, raw OCR output, corrected name, correction score, status flag
Header filter excludes top 35% of the image to avoid clinic letterhead false positives.
PharmaSafe OCR
10

## Slide 11
Pipeline test-set results
111 images processed across FAST NUCES and UEM test sets
Detected boxes, average confidence and top corrected names
1,213
total detections
554
medicine_name boxes
417
medicine_dose boxes
242
medicine_type boxes
106 of 111 images produced at least one detection. TrOCR returned non-empty output for all 1,213 crops.
PharmaSafe OCR
11

## Slide 12
Limitations and future work
The main bottleneck is data fragmentation, not model architecture
CURRENT LIMITATIONS
• No single public dataset covers detection, OCR and standardized names together • Cross-dataset domain gap between YOLO crops and TrOCR word-level training data • Numeric dosage OCR remains difficult • English drug-name coverage only; multilingual text is degraded
HIGHEST-IMPACT NEXT STEPS
• Build a unified prescription dataset with boxes, OCR text and standard mappings • Train larger YOLO variants when more data is available • Add multilingual OCR for Bengali / Urdu scripts • Use active learning with pharmacist verification • Explore pharmacological language models for correction
Future direction: human-in-the-loop validation and wider language coverage
PharmaSafe OCR
12

## Slide 13
Key takeaways
A traceable pipeline for prescription information extraction
Detect
Read
Correct
Review
PharmaSafe combines YOLO11n, TrOCR and domain-aware fuzzy correction to transform handwritten prescriptions into structured medication data with inspectable intermediate outputs.
Best current path forward: create a unified dataset and add pharmacist-in-the-loop correction to continuously improve the system.
PharmaSafe OCR
13